## Slide 1: A Portable Lab Kit for Teaching Introduction to Logic Circuits & Logic Design
Brock J. LaMeres Associate Professor Department of Electrical & Computer Engineering Montana State University - Bozeman

## Slide 2: Course Overview
Logic Circuits & Logic Design are found in nearly every ABET accredited electrical engineering and computer engineering programs.
These topics are also popular electives for computer scientists & mechanical engineers.

## Slide 3: Typical Topics
Classical Digital Design
    Number Systems
    Digital Circuit Operation
    Boolean Algebra
    Combinational Logic Design
    MSI Logic
    State Machines

## Slide 4: Typical Topics
Modern Digital Design
    Hardware Description Languages (VHDL, Verilog)
    HDL Modeling Techniques (concurrency, sequential, structural, RTL)
    Memory Devices
    Arithmetic Circuits
    Programmable Logic
    Computer Systems

## Slide 5: Moving This Content Online
The Lecture - Relatively straight forward…
Reading
Assignments
Lecture Videos using DocCam or Screen Capture
Online Homework Assessments

## Slide 6: Moving This Content Online
The Laboratory… - This is where the challenge is… - Our Requirements:
  Portable
  Low Cost
  Experience with classical & modern design flows
  Experience with measurement techniques

## Slide 7: Portable Lab Kit
Our Kit Consists of Three Items 1) A breadboard and an assortment of discrete parts & I/O ($25)
74HC Series parts (ANDs, ORs, etc). These provide experience with interfacing and circuit operation using very little power.
Basic I/O in the form of LEDs, switches, buzzers, 7-segment displays. These provide visual/auditory feedback on the circuit operation.
This helps teach the concepts of classical digital design.

## Slide 8: Portable Lab Kit
Our Kit Consists of Three Items 2) Terasic DE0-nano FPGA Board ($60) purchased 2 years ago. Now ~$90.
Free Altera Quartus software allows HDL-based designs to be fully implemented and downloaded to FPGA.
FPGA board can be interfaced with breadboard I/O.
This helps teach the concepts of modern digital design.

## Slide 9: Portable Lab Kit
Our Kit Consists of Three Items 3) Digilent Analog Discovery ($99) purchased 2 years ago. Now ~$179.
USB-based instrument that provides: power supply, AWG, Volt Meter, Logic Analyzer, & Oscilloscope.

## Slide 10: Student Demo’s
Demo’s taken by uploading videos or using Google Hangouts
Google Hangout

## Slide 11: Pros and Cons
Pros
This approach has been successfully used for the past four semesters at MSU.
The kit is full portable with an original cost of $185.
Course offerings have been extended state-wide. Last semesters we had students from MSU-Bozeman, MSU-Billings, and Flathead Valley Community College.
This approach is being used to address large enrollments that are exceeding classroom & lab capacity.
This approach allows the course to be offered spring, fall, and summer to help students meet key pre-requisite chains.

## Slide 12: Pros and Cons
Cons
Product obsolescence. The Analog Discovery now has a version 2. The DE0-nano has been replaced. This has impact on kit maintenance and keeping lab handouts/videos up to date.
Cost. The original $99 Analog Discovery cost is no longer available. It is now $179 (academic). The DE0-nano now costs $90 since it is being obsoleted. The replacement (DE0-CV costs $99). Cost creep could eventually make this unsustainable at smaller public universities.

## Slide 13: Summary
This portable kit has enabled a fully online offering of a logic circuits class including laboratory component.
No significant difference in student understanding has been measured.
This work was supported through NSF DUE Awards IDs 0836961 and 1432373.