## Slide 1: Principles of Audio System Grounding and Signal Integrity
Rob Maher
Department of Electrical and Computer Engineering Montana State University-Bozeman
Presentation for 2015 Joint Engineers Conference

## Slide 2: Agenda
Noise and interference: what is it?
Introduction – basic principles of residential and light-commercial AC power
Interconnection – analog signal integrity in audio interconnection cables
Sources of interference – inductive/magnetic coupling, capacitive/electric coupling
What to do to find and eliminate problems
Conclusions

## Slide 3: Disclaimer
This is NOT an authoritative lecture or training session about the National Electrical Code!
  Some or all of you may know more about the NEC than I do!
  Designers and installers must consult and follow the Code, and use qualified, licensed personnel.
  Whenever there is a doubt, consult with a knowledgeable, licensed electrician.

## Slide 4: Some material taken from:
Bill Whitlock, President, Jensen Transformers
“An Overview of Audio System Grounding and Interfacing,” September, 2012, Audio Engineering Society Central Indiana Section.
https://centralindianaaes.files.wordpress.com/2012/09/indy-aes-2012-seminar-w-notes-v1-0.pdf

## Slide 5: Grounding and Interfacing
Many myths and misinterpretations
  Cables don’t magically “pick up” noise
  The “earth” is not a magically perfect “ground”
  Better “shielding” is not always the answer
  Just because a box or cable is expensive does not mean it has good interconnect properties
  Physics is not negotiable!

## Slide 6: Electrical Noise
ALL electronic materials and devices have inherent noise.
  Johnson/Thermal noise: vrms=√(4kTRΔf) e.g., 10k resistor, 20kHz bandwidth, @ room temp: vrms= 1.8 µV.
Dynamic Range: Ratio of the maximum undistorted output signal to the residual output noise, or “noise floor.” Good audio systems require 120dB range (ratio 106).

## Slide 7: Electrical Noise (cont.)
Once in-band noise becomes part of an analog signal, it is essentially impossible to remove it.
Therefore, the weakest link principle applies: the dynamic range of an audio system is constrained by the dynamic range of each stage.

## Slide 8: Things to remember…
Circuit principles are key: identify the circuit and all AC-coupled and DC-coupled paths.
The protective ground (third prong) is there for life safety protection. Engineers shall NEVER defeat this purpose.
Always employ good gain structure: never attenuate a signal that will have to be amplified again later in the audio chain.

## Slide 9: Residential Power in U.S.A.

## Slide 10: Residential 3-Wire Service

## Slide 11: What’s up with “GROUND”?
Unfortunately, the use of the term “ground” is widely used to refer to a common return path in a circuit. It almost never literally means the physical earth (soil) ground, unless this is clearly stated.
The ONLY reasons physical earth (soil) ground is considered is lightning protection and antenna (ground plane) propagation.

## Slide 12: Mythical Soil
A common statement by some audiophiles is that earth ground is essential for good quality sound.
Apparently the earth can suck up all the stray electronic noise?
Soil is generally a very poor conductor: not something with magical properties!

## Slide 13: What’s up with “GROUND”? (cont.)
Automobiles have audio systems: are they grounded to the earth?
Portable battery-powered electronics: is an earth ground necessary?
Aircraft (and spacecraft!) have electronics: is an earth ground used? Of course not!

## Slide 14: Why we use three wires:

## Slide 15: Protective Ground
NOTE that the protection comes from the circuit loop wiring and the circuit breaker: the physical soil of the earth is NOT involved in the protective action AT ALL.
The soil/earth ground provides a path for lightning to discharge before entering the premises. It is not essential for audio equipment at all.

## Slide 16: Watch out: the 3-to-2 Adapter
Some old residential electrical systems have two-prong outlets. In SOME cases the outlet box is served by metal conduit that is bonded to the ground bus at the service panel. A 3-to-2 adapter can be used to provide the protective ground continuity required by a three-prong appliance.

## Slide 17: 3-to-2 Adapter (cont.)
HOWEVER, some individuals may try to remedy noise interference issues by “lifting” the protective conductor of a three-prong device by deliberately using the adapter with the ground NOT connected.
If an engineer does this and there was a fire or injury in a system connected this way—the engineer is legally liable! NEVER do this!

## Slide 18: A Particularly Bad Scenario
One device has 3-prong power cable, connected to another device with a ground “lifter” in place.
When a fault occurs in the “lifted” device, the resulting fault current can flow in the interconnect cable, likely causing it to overheat, melt, and catch fire.

## Slide 19: GFCI
If a protective safety ground is not available, always use a Ground Fault Circuit Interrupter (GFCI).
By code, a GFCI need not have an actual protective ground wire back to the service panel.

## Slide 20: Myths vs. Facts
“A stout copper wire has zero impedance”
  In fact, a wire will have finite DC resistance (milliohms per foot), and finite inductive impedance (jωL). The inductive impedance of a power conductor wire may be tens of ohms in the AM radio frequency band.
  Inductance doesn’t depend much upon the diameter of the wire.

## Slide 21: Myths vs. Facts (cont.)
“All earth/protective grounds need to be at zero volts, so use lots of ground rods.”
  In fact, soil resistance between separated ground rods is tens or hundreds of ohms (!), and varies with soil conditions, moisture, corrosion, etc. A wire connecting the ground rods will have a much lower resistance—and this is required by the code!

## Slide 22: Myths vs. Facts (cont.)
“A ground loop is the fault of protective ground wires.”
  In fact, a ground loop is caused by ALL signal interconnection wiring, and so choosing an interconnection that is immune to ground loop issues is the solution, NOT eliminating protective grounds.

## Slide 23: NEVER NEVER NEVER!!

## Slide 24: Audio Circuit Review
Goal of interface: maximize voltage transfer (not power transfer)
Current requires a circuit: audio frequency noise is due to current in the interface, and electric and magnetic field coupling.
Nominal consumer level: 316 mV rms
Nominal professional level: 1.23 V rms

## Slide 25: Audio Interconnect: 2 conductor (no earth ground)

## Slide 26: Audio Interconnect: 3 conductor (earth ground)

## Slide 28: Unbalanced Interconnect: Inherently Noisy

## Slide 29: Some numbers…

## Slide 30: Audio cables: Check specs
Belden 8412
20 AWG stranded
0.59 uH/m
98.4 pF/m
Shield DC R: 10 ohm/km
Belden 2221
26 AWG stranded
0.55 uH/m
42.7 pF/m
Shield DC R: 21.6 ohm/km
Belden 8451
22 AWG stranded
0.56 uH/m
112 pF/m
Shield DC R: 47.6 ohm/km
Belden 1883
24 AWG stranded
0.56 uH/m
101.7 pF/m
Shield DC R: 60.7 ohm/km

## Slide 31: Coupling to Protective Ground

## Slide 32: Solution: Audio Transformer

## Slide 33: Wiring Error: BIG Noise Issue

## Slide 34: Thank you