## Slide 1: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.1 Analog to Digital Converters - Overview

## Slide 2: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
Analog-to-Digital Converter (ADC or A2D) – a circuit that takes in an analog voltage and produces a digital representation of its value.

## Slide 3: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
time

## Slide 4: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
Sample – the action of duplicating the voltage value of the input signal.
Hold – the action of holding the voltage for a brief amount of time by use of a capacitor.
time

## Slide 5: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The Sample is accomplished by momentarily connecting the signal to a capacitor in order to charge it up to the same voltage.
The Hold is accomplished by disconnecting the signal and allowing the conversion to be conducted on the voltage on the capacitor.
time

## Slide 6: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The Sample-and-Hold circuitry is designed so that this can be accomplished very quickly so that it can disconnect from the input signal as soon as possible to avoid altering its signal integrity.
time

## Slide 7: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
Input Voltage Range – The voltage is digitized within a range of voltages from:
  Voltage Reference High (VR+)
  Voltage Reference High (VR-)
time
VR+
VR-

## Slide 8: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The goal of the conversion is to convert the analog voltage into a digital number.
This is called digitizing, quantizing, or discretizing.
time
VR+
VR-

## Slide 9: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
n represents the number of bits in the digital value of the conversion.
time
VR+
VR-
0
1
n=1
Sample=0

## Slide 10: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
n represents the number of bits in the digital value of the conversion.
The input voltage range is divided into 2n discrete zones.
time
VR+
VR-
0
1
n=1
Sample=0

## Slide 11: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The larger the n, the closer the digital value is to the actual analog voltage.
time
VR+
VR-
0
1
n=1
Sample=0

## Slide 12: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The larger the n, the closer the digital value is to the actual analog voltage.
time
VR+
VR-
00
n=2
01
10
11
Sample=01

## Slide 13: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The larger the n, the closer the digital value is to the actual analog voltage.
time
VR+
VR-
n=3
Sample=010
000
001
010
011
100
101
110
111

## Slide 14: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The larger the n, the closer the digital value is to the actual analog voltage.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 15: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The number of bits n is called the ADC’s resolution.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 16: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The number of bits n is called the ADC’s resolution.
MCU’s typically have ADC’s with resolutions of 8 to 16 bits.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 17: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The number of bits n is called the ADC’s resolution.
MCU’s typically have ADC’s with resolutions of 8 to 16 bits.
The MSP430 has up to 12-bits of resolution.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 18: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The precision of an ADC is the smallest voltage that the LSB of the digital output can represent.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 19: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The precision of an ADC is the smallest voltage that the LSB of the digital output can represent.
This is found by dividing the input voltage range by the number of discrete zones.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 20: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
time
VR+
VR-

## Slide 21: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The original analog value is found by multiplying the digital conversion result (NADC) with the resolution.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 22: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
time
VR+
VR-
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 23: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The accuracy is how close the digital output is to the input signal.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 24: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The accuracy is how close the digital output is to the input signal.
By design, an ADC will only ever be able to get within +/- ½ LSB of the original analog value.
time
VR+
VR-
n=4
Sample=0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 25: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
time
VR+
VR-
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 26: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111

## Slide 27: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
time

## Slide 28: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
time

## Slide 29: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
time

## Slide 30: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
time

## Slide 31: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
time

## Slide 32: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110

## Slide 33: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The voltage can be sampled over time to create a list of digital values.
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110
1101

## Slide 34: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The sample period (TSA) is the time between samples.
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110
1101
TSA

## Slide 35: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The sampling rate is the frequency of sampling: fSA= 1/TSA
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110
1101
TSA

## Slide 36: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The sampling rate is the frequency of sampling: fSA= 1/TSA
This has units of samples-per-second (i.e., ksps, Msps).
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110
1101
TSA

## Slide 37: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
If you sample fast enough, you can reconstruct the original signal.
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110
1101

## Slide 38: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
If you sample fast enough, you can reconstruct the original signal.
Nyquist-Shannon Sampling Theorem states you need to sample at least twice as fast as the frequency of the incoming signal to accurately reconstruct the original waveform.
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110
1101

## Slide 39: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
The MSP430FR2355 can sample up to 200 ksps.
time
VR+
VR-
n=4
0100
0000
0010
0100
0110
0001
0011
0101
0111
1001
1011
1101
1000
1010
1100
1110
1111
1000
0111
0101
1001
1101
1110
1101

## Slide 40: Ch. 15: Analog to Digital Converters
15.1 Analog to Digital Converters
15.1 Analog to Digital Converters
12-bit Example

## Slide 41: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.1 Analog to Digital Converters - Overview
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 42: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 - Configuration

## Slide 43: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355

## Slide 44: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355

## Slide 45: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The MSP430 contains an ADC core with selectable resolution (8-bit, 10-bit, 12-bit).

## Slide 46: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC can be driven with 1 of 16 inputs that are selected using an analog multiplexer that sits in front of the ADC core.

## Slide 47: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC can be driven with 1 of 16 inputs that are selected using an analog multiplexer that sits in front of the ADC core.
A0  A11 are connected to pins that share with ports (use Port Function Select Registers = 11).

## Slide 48: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC can be driven with 1 of 16 inputs that are selected using an analog multiplexer that sits in front of the ADC core.
A0  A11 are connected to pins that share with ports (use Port Function Select Registers = 11).
A12 is an on-chip temperature sensor

## Slide 49: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC can be driven with 1 of 16 inputs that are selected using an analog multiplexer that sits in front of the ADC core.
A0  A11 are connected to pins that share with ports (use Port Function Select Registers = 11).
A12 is an on-chip temperature sensor
A13 is the internal voltage reference.

## Slide 50: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC can be driven with 1 of 16 inputs that are selected using an analog multiplexer that sits in front of the ADC core.
A0  A11 are connected to pins that share with ports (use Port Function Select Registers = 11).
A12 is an on-chip temperature sensor
A13 is the internal voltage reference.
A14 and A15 are VSS and VCC.

## Slide 51: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC clock source is selectable with two stages of programmable dividers/prescalers.

## Slide 52: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC clock source is selectable with two stages of programmable dividers/prescalers.
Note: The ADCCL frequency is NOT the sample rate. The sample/convert takes multiple clock settings.

## Slide 53: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The voltage range of the ADC is also programmable with options of using the power supply (VCC) and GND (VSS), input pins, or a variety of internally generated voltages.

## Slide 54: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC peripheral also has a large number of programmable options that dictate its behavior in addition to 6 interrupts that can be triggered upon certain conditions.

## Slide 55: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The basic use model for the ADC peripheral is:
  Configure peripheral using a set of registers.
  The conversation is started by the user (or by the successful completion of a prior conversation).
  The result of the conversation is ready from the ADC’s conversion memory register.

## Slide 56: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
Flags can be used to track the status of the conversion and trigger interrupts to react to various states of the conversion.

## Slide 57: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
Image Courtesy of https://neodem.wp.horizon.ac.uk/
ADC Control 0 (ADCCTL0) Register
ADC Control 1 (ADCCTL1) Register
ADC Control 2 (ADCCTL2) Register
ADC Memory Control (ADCMCTL0) Register
ADC Conversion Memory (ADCMEM0) Register
ADC Interrupt Enable (ADCIE) Register
ADC Interrupt Flag (ADCIFG) Register
ADC Interrupt Vector (ADCIV) Register
ADC Window Comparator Low Threshold (ADCLO) Register
ADC Window Comparator High Threshold (ADCHI) Register

## Slide 58: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL0 contains:
settings for the number of ADCCLK cycles to use during the conversion (ADCSHTx)
how the ADC is triggered (ADCMSC)
turning the ADC on (ADCON)
enabling the conversion (ADCENC)
Starting a conversion (ADCSC).

## Slide 59: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL0 contains:
settings for the number of ADCCLK cycles to use during the conversion (ADCSHTx)
how the ADC is triggered (ADCMSC)
turning the ADC on (ADCON)
enabling the conversion (ADCENC)
Starting a conversion (ADCSC).
The ADCENC and ADCSC bits are used to start a conversion by asserting them simultaneously.
The ADCENC and ADCSC bits are used to start a conversion by asserting them simultaneously.

## Slide 60: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL0
We will use the following for the basic ADC setup

## Slide 61: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL0
We will use the following for the basic ADC setup
We’ll assert these to start a conversion.

## Slide 62: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL1 contains:
settings for the source of the sample trigger (ADCSHSx)
an option for running the sampler in pulse mode (ADCSHP)
an input inversion option (ADCISSH)
settings for the second clock divider stage (ADCDIVx)

## Slide 63: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL1 contains:
the ADC clock source (ADCSSELx)
whether the conversion is to run once or multiple times upon a trigger (ADCCONSEQx)
a status flag indicating the conversion is busy (ADCBSUSY).

## Slide 64: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL1
We will use the following for the basic ADC setup

## Slide 65: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL2 contains:
settings for the first clock divider stage (ADCPDIVx)
the resolution of the ADC (ADCRES)
the data format of the result (ADCDF)
the range for the anticipated sample rate (ADCSR).

## Slide 66: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL2 contains:
settings for the first clock divider stage (ADCPDIVx)
the resolution of the ADC (ADCRES)
the data format of the result (ADCDF)
the range for the anticipated sample rate (ADCSR).
Note that the default setting for ADCRES is 01 (10-bit).
If this setting is to be changed, the LSB of ADCRES needs to be cleared before the new settings are written.

## Slide 67: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCCTL2
We will use the following for the basic ADC setup

## Slide 68: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCMCTL0 contains:
settings for the reference voltage selection (ADCSREFx).
  “VREF” – refers to the internal reference voltages that the MCU can produce.
  “VEREF+/-” – refers to the external pins.
  “AVCC” – refers to the MCU power supply (+3.4v).
the ADC input channel that will be routed to the sample-and-hold stage (ADCINCHx).

## Slide 69: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCMCTL0 contains:
settings for the reference voltage selection (ADCSREFx).
  “VREF” – refers to the internal reference voltages that the MCU can produce.
  “VEREF+/-” – refers to the external pins.
  “AVCC” – refers to the MCU power supply (+3.4v).
the ADC input channel that will be routed to the sample-and-hold stage (ADCINCHx).
Note: the Port Function Select settings of 0b11 selects the Analog function.

## Slide 70: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
ADCMCTL0
We will use the following for the basic ADC setup

## Slide 71: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
The ADC peripheral contains six interrupt flags that can be used to monitor the status of the conversion.

## Slide 72: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
There is an interrupt flag that will trigger when a conversion is complete (ADCIFG0).

## Slide 73: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
There are three interrupts that can be used with a threshold window feature where the ADC watches for whether the input is within the window (ADCINIFG), below the window (ADCLOIFG), or above the window (ADCHIIFG).

## Slide 74: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
There is also one interrupt to indicate if ADCMEM0 has been written to before the last conversion result has been read (ADCOVIFG).

## Slide 75: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355
Finally, there is one interrupt to indicate that a new conversion is triggered before the current conversion has completed (ADCTOVIFG).

## Slide 76: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355

## Slide 77: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
15.2 ADC Operation on the MSP430FR2355

## Slide 78: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 - Configuration
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 79: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 – Example: Reading an Analog Voltage using Polling Conversion-Complete IFG

## Slide 80: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using Polling to Monitor Conversion-Complete

## Slide 81: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using Polling to Monitor Conversion-Complete
Note: the Port Function Select settings of 0b11 selects the Analog function.

## Slide 82: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using Polling to Monitor Conversion-Complete
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_ADC_Sampling_P1.2_Polling
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 83: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using Polling to Monitor Conversion-Complete

## Slide 84: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using Polling to Monitor Conversion-Complete
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Step 3: Save, debug, and run your program. Also run your function generator to produce the sine wave on P1.2.

## Slide 85: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 – Example: Reading an Analog Voltage using Polling Conversion-Complete IFG
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 86: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 – Example: Reading an Analog Voltage using Polling Conversion-Complete IRQ

## Slide 87: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete

## Slide 88: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete

## Slide 89: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
We’ll first setup the Port Function Select registers to use the Analog input on P1.2.
P1SEL1(2):P1SEL(0)=11

## Slide 90: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
ADCCTL0
ADCSHT = 10; Conversion cycles = 16
ADCON = 1; Turn ADC On

## Slide 91: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
ADCCTL1
ADCSSEL = 10; SMCLK
ADCSHP = 1; Use ADC for trigger

## Slide 92: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
ADCCTL2
ADCRES = 10; 12-Bit

## Slide 93: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
ADCMCTL0
ADCINCH = 0010; Use A2

## Slide 94: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
Notable Default Settings
VR+ = VCC, VR- = GND
Prescalars = 1
Format = Unsigned
Single Conversion / Channel

## Slide 95: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
Our Design
Start conversion by: ADCENC = 1, ADCSC= 1.
Use ADCIFG0 to trigger IRQ when complete.
Vector = ADC_VECTOR.

## Slide 96: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_ADC_Sampling_P1.2_IRQ
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.

## Slide 97: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
Step 3: Save, debug, and run your program. Also run your function generator to produce the sine wave on P1.2.

## Slide 98: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 – Example: Reading an Analog Voltage using Polling Conversion-Complete IRQ
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 99: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 – Example: Reading Analog Voltage w Conversion-Complete IRQ & LPM

## Slide 100: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM

## Slide 101: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM

## Slide 102: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM
We’ll first setup the Port Function Select registers to use the Analog input on P1.2.
P1SEL1(2):P1SEL(0)=11

## Slide 103: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM
ADCCTL0
ADCSHT = 10; Conversion cycles = 16
ADCON = 1; Turn ADC On

## Slide 104: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM
ADCCTL1
ADCSSEL = 10; SMCLK
ADCSHP = 1; Use ADC for trigger

## Slide 105: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM
ADCCTL2
ADCRES = 10; 12-Bit

## Slide 106: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM
ADCMCTL0
ADCINCH = 0010; Use A2

## Slide 107: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM
Notable Default Settings
VR+ = VCC, VR- = GND
Prescalars = 1
Format = Unsigned
Single Conversion / Channel

## Slide 108: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading Analog Voltage w Conversion-Complete IRQ & LPM
Our Design
Start conversion by: ADCENC = 1, ADCSC= 1.
Go into LPM0 (MCLK dis, SMCLK en)
Use ADCIFG0 to trigger IRQ when complete.
Vector = ADC_VECTOR.

## Slide 109: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ and Low Power Mode
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_ADC_Sampling_P1.2_LPM
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 110: Ch. 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355
Reading an Analog Voltage With the ADC Using an IRQ to Monitor Conversion-Complete
Step 3: Save, debug, and run your program. Also run your function generator to produce the sine wave on P1.2.

## Slide 111: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 15: Analog to Digital Converters
15.2 ADC Operation on the MSP430FR2355 – Example: Reading Analog Voltage w Conversion-Complete IRQ & LPM
www.youtube.com/c/DigitalLogicProgramming_LaMeres