## Slide 1: Reconfigurable Computing for Space Applications
Dr. Brock J. LaMeres
Associate Professor
Electrical & Computer Engineering

## Slide 2: What is Reconfigurable Computing
A System That Alters Its Hardware as its Normal Operating Procedure
  This can be done in real-time or at compile time.
  This can be done on the full-chip, or just on certain portions.
  Changing the hardware allows it to be optimized for the application at hand.
Today’s Computers are Based on a General-Purpose Processor
  The GP CPU is designed to do many things.
  This is the “Jack of All Trades, Master of None” approach.
General Purpose CPU Model
Reconfigurable Computing Model

## Slide 3: Who Cares?
Our Existing Computers Seem to be Working Well. Why Change?
  Our existing computers have benefited from 40 years of Moore’s Law.
  In the 1960’s, Gordon Moore predicted that the number of transistors on a chip would double every ~24 months.
Gordon Moore, co-founder of Intel, holding a vacuum tube.
1959 - 1965
1971* - 2011
Note: First microprocessor introduced in 1971,
the Intel 4004 with 2300 transistors.
Intel 4004 (2300 T)
Intel Xeon (2B T)

## Slide 4: How long can we do this?
When will Moore’s Law End?
  Most exponentials do come to an end.
Clock Speed
Power
Performance per Clock Cycle
But is transistor count what we care about?

## Slide 5: Computation vs. Transistor Count
We Really Care About Computation
You Are Here

## Slide 6: How Does This Relate to Space?
We Discovered After Beginning this Research That:
  Our approach helps mitigate radiation induced faults in computers.
  Our approach allows commercial parts to be used in space = low cost
You Are Here

## Slide 7: So We Began Building Space Computers
FPGA-Based, Radiation Tolerant Computer
  The FPGA is divided up into Tiles
  A Tile is a quantum of resources that:
      Fully contains a system (e.g., processor, accelerator)
      Can be programmed via partial reconfiguration (PR)
Fault Tolerance
  TMR + Spares
  Spatial Avoidance of Background Repair
  Scrubbing
  An External Radiation Sensor
16 Tile System on an Xilinx Virtex-6

## Slide 8: Technical Readiness Level (TRL-1)
Step 1 – Build a Prototype to See if it is Possible
  The Montana Space Grant Consortium funds an investigation into conducting radiation tolerant computing research at MSU. The goal is to understand the problem, propose a solution, and build relationships with scientists at NASA.
(2008-2010)
Proof of Concept
Timeline of Activity at MSU
Clint Gauer (MSEE from MSU 2009) demo’s computer to MSFC Chief of Technology Andrew Keys
2010
2011
2012
2013
2014-16
2016
2017
2009
2008

## Slide 9: Technical Readiness Level (TRL-3)
Step 2 –Test in a Cyclotron
  NASA EPSCoR funds the development of a more functional prototype and testing under bombardment by radiation at the Texas A&M Radiation Effects Facility.
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
(2010-2012)
Timeline of Activity at MSU
Ray Weber (Ph.D., EE from MSU, 2014) prepares experiment.
2010
2011
2012
2013
2014-16
2016
2017
2009
2008
MSU Computer

## Slide 10: Technical Readiness Level (TRL-5)
Step 3 – Demonstrate as Flight Hardware on High Altitude Balloons
  NASA Education Office funds the development of the computer into flight hardware for demonstration on high altitude balloon systems, both in Montana and at NASA.
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
(2010-2012)
(2011-2013)
Timeline of Activity at MSU
MSU Computer
Justin Hogan (Ph.D., EE from MSU, 2014) prepares payload.
2010
2011
2012
2013
2014-16
2016
2017
2009
2008

## Slide 11: Technical Readiness Level (TRL-6)
Step 4 – Demonstrate as Flight Hardware on a Sounding Rocket
  NASA OCT & FOP fund the demonstration of the computer system on sounding rocket.
  Flew on UP Aerospace SpaceLoft-9 in Oct 2014. Upcoming flight at Wallops in Mar-16.
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
(2010-2012)
(2011-2013)
(2012-2016)
Timeline of Activity at MSU
2010
2011
2012
2013
2014-16
2016
2017
2009
2008
MSU Computer

## Slide 12: Technical Readiness Level (TRL-7)
Step 5 – Demonstrate on the International Space Station
  NASA EPSCoR funds the demonstration of computer system on ISS
(2008-2010)
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
(2010-2012)
(2011-2013)
(2012-2016)
(2014-2016)
Timeline of Activity at MSU
2010
2011
2012
2013
2014-16
2016
2017
2009
2008

## Slide 13: Technical Readiness Level (TRL-8)
Step 6 – Demonstrate as a Stand-Alone Satellite
  NASA SmallSat Technology Partnership Program (SSTP) funds the development of a stand-alone satellite for LEO mission.
  This work is being conducted through a partnership between MSU & GSFC.
(2008-2010)
2010
2011
2012
2013
2014-16
2016
2017
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
Satellite
Demo
(2010-2012)
(2011-2013)
(2012-2016)
(2014-2016)
(2014-2017)
2009
2008
Timeline of Activity at MSU
Artix-7 Implementation
Re-using Avionics from FIREBIRD-II

## Slide 14: What Are We Working On Now?
1. A 2nd Sounding Rocket Flight at NASA Wallops in March 2016
A Flight to the International Space Station in June of 2016
Building our Satellite for a Launch in 2017
Thinking about “what’s next”

## Slide 15: What Do My Students Do?
Everything was Designed and Built By MSU Students!
Todd Buerkle, Justin Hogan, Ray Weber at Johnson Space Center for demo, 2012.
Todd Buerkle, Jennifer Hane at the Marshall Space Flight Center, 2011.
Justin Hogan at the NASA Columbia Scientific Balloon Facility, 2012.
Justin Hogan & Ray Weber featured in MSU News Story, 2012.
Clint Gauer demo’s computer at Marshall Space Flight Center, 2009.
Todd Buerkle & Jennifer Hane demo computer at Marshall Space Flight Center, 2012.
Clint Gauer at Marshall Space Flight Center for demo, 2009.
Kaysha Young prepares payload for balloon flight, 2012.
2013 balloon team recovers payload in front of moose, 2013.
2011 balloon team featured in MSU news story, 2011.

## Slide 16: Questions
MSU Computer
MSU Computer