## Slide 1
Objective
This study observed EMS worker restraint usage feasibility while performing the most common procedures.
Methods
Rural EMS Worker Restraint Usage and Feasibility in Emergency Response Vehicles
Tawny Hoyt1, Dr. Laura Stanley1, Nels Sanddal2, and Teri Sanddal2
1Western Transportation Institute – Montana State University Bozeman and 2Critical Illness and Trauma Foundation, Bozeman, MT
Literature Cited:
1 "Ambulance Crash-Related Injuries Among Emergency Medical Services Workers –United States, 1991 - 2002." Journal of American Medical Association, 2 Apr.2003. Web. 25 Sept. 2009. <http://jama.amaassn.org/cgi/content/full/289/13/1628>.
2 "NAEMSP Releases Ambulance Safety Data." EMS Responder, 1 July 2009. Web. 30 Sept. 2009. <http://emsresponder.com/features/article.jsp?id=9805&siteSection=25>.
3Gilad, Issachar, and Eyal Byran. “Ergonomic Evaluation of the Ambulance Interior to Reduce Paramedic Discomfort and Posture Stress.” Human Factors: The Journal of the Human Factors and Eronomics Society.” (2007) 49, 1019.
Chart: Reported Restraint Usage in Patient Compartment3
| Always wear seatbelt | Only wear on administrative rides | Never wear seatbelt | Wear seatbelt but not when performing procedures
Frequency | 3 | 40 | 40 | 17
So why are medics riding unrestrained during emergency transport situations?
Medics report the inability to access patient and provide proper care as the primary reason3. In this way it is the procedures that are required of the EMS workers may cause them to ride unrestrained.
Background
Emergency medical service (EMS) workers have a fatality rate of 12.7 per 100,0001. Of these fatalities, 74% of them are transportation related2.
A task analysis is method of documenting how a user (EMS worker) moves through a system (procedural completion). Task analyses were conducted for each of the common procedures in transport situations. This was used to understand duties and body postures during these procedures.
Pareto Analysis
Mock Up Presentations
Task Analysis
Mock up presentations performed by two experienced EMS workers (male - paramedic, 32 years old with 11 years experience; male – EMT-Basic, 60 years old with 35 years experience) were filmed to further understand procedures outlined in Pareto analysis. Analysis was conducted inside a Ford F-150 model ambulance.
A Pareto analysis is a statistical technique of selecting significant factors in a system. This method was used to determine common procedures during transport.
Chart: BLS Treatment
| Prime Survey | Second Survey | Monitor Vitals | Spinal Precautns | Monitor Exist IV | Bndg./Hem. Cntrl. | Splint - Rigid | BVM - Asst Vent. | Arwy - Orl//Nas. | Airwy - Man. | CPR | Suction | Extrication | Restraints | Splint Traction | AED | Psych. Assist | Hyperventilated | Abd./Chest Thrust | Irrigation | OB Delivery | PASG
Frequency | 0.30821 | 0.30181 | 0.28996 | 0.032321 | 0.019222 | 0.0094559 | 0.0090296 | 0.0049992 | 0.0049217 | 0.0040691 | 0.0040304 | 0.0037979 | 0.0025965 | 0.0022865 | 0.00085258 | 0.00081383 | 0.00081383 | 0.00038754 | 0.00023252 | 0.00015501 | 3.8754e-05 | 0
Cum Percentage | 0.30821 | 0.61002 | 0.89998 | 0.9323 | 0.95152 | 0.96098 | 0.97 | 0.975 | 0.97993 | 0.98399 | 0.98803 | 0.99182 | 0.99442 | 0.99671 | 0.99756 | 0.99837 | 0.99919 | 0.99957 | 0.99981 | 0.99996 | 1 | 1
Chart: ALS Treatment
| Pulse Oximetry | IV - Peripheral | Glucometer | Cardiac Monitor | Blood Drawn | Medication Admin. | 12-Lead EKG | Intubation - Oral | End Tidal CO2 | Defibrillation | Cardiac Magnet | ET Suction | Intraosseous | IV - Ext. Jugular | Pacing | Chest Dec. | Rescue Airway | Vagal Maneuver | Cardiovert | Magill Forceps | Gastric Tube | Intubation - Nasal | Ventilator | CPAP | Crico/Trach | Heparin/Sal Lock | LMA
Frequency | 0.25565 | 0.1955 | 0.15753 | 0.11643 | 0.11434 | 0.099734 | 0.041886 | 0.0049032 | 0.0037557 | 0.0025559 | 0.0014084 | 0.0014084 | 0.00099108 | 0.00093892 | 0.00078243 | 0.00067811 | 0.00062595 | 0.00026081 | 0.00020865 | 0.00015649 | 0.00010432 | 0.00010432 | 5.2162e-05 | 0 | 0 | 0 | 0
Cum Percentage | 0.25565 | 0.45115 | 0.60868 | 0.72511 | 0.83944 | 0.93918 | 0.98107 | 0.98597 | 0.98972 | 0.99228 | 0.99369 | 0.9951 | 0.99609 | 0.99703 | 0.99781 | 0.99849 | 0.99911 | 0.99937 | 0.99958 | 0.99974 | 0.99984 | 0.99995 | 1 | 1 | 1 | 1 | 1
Reach Envelope Analysis
Reach envelopes were created for three population percentiles (5th percentile female, 50th percentile male, and 95th percentile male) and computer aided drawings were created to assess the reach feasibility of seated and restrained medics.
Reach envelopes for 50th percentile male
Zone of convenient reach: Task Feasibility
Maximum reach: Equipment Access Feasibility
A reach envelope is the area in which the performance of manual tasks can be completed conveniently, or at all, by a seated, restrained medic.
Envelopes were created from the diagram at left where b is the biacromial breadth and r is the radius of reach.
Chart: Reach Feasibility
| Percentage of Feasible Equipment Access | Percentage of Time Feasibly Restrained
5th %ile Female | 42 | 34
50th %ile Male | 52 | 42
95th %ile Male | 73 | 59
Feasibility varies by population percentile. However, on average restraint usage is feasible 42% of the time the patient is being treated.
Acknowledgements
We would like to thank the Critical Illness and Trauma Foundation for their support. Also, Brian Carroll and Jessica Mueller for their contributions to this project. We would like to acknowledge the American Medical Response in Bozeman for their assistance. Finally, thank you to the Western Transportation Institute supporting this effort.
Conclusions
Restraint use is feasible for an average of 42% of the time the patient is being treated. With simple design modifications (e.g. relocation of IV bag hook, placement of medication admin equipment) this can be increased to 50% of the patient treatment time. These improvements would increase safety of medics riding in the rear of the ambulance
b
r
The primary cause of transportation related deaths is the lack of restraint use in the patient compartment of the ambulance. A recent survey of working medics showed that only 3% of medics report actually wearing their seatbelts all the time3.
Results
Overhead ambulance layout was created from measurements of in use ambulance.
The envelopes were then laid over the overhead drawing of the ambulance to assess restraint feasibility.